Environmental Health and Safety

VIRGINIA POLYTECHNIC INSTITUTE

AND STATE UNIVERSITY

Phone 540-231-2509 Fax 540-231-3944

Email: spvaler@vt.edu

www.ehss@vt.edu

Information for N, R, and P Particulate Respirator Categories

N, R, and P are NIOSH certification categories that apply to negative pressure air-purifying respirators that protect against respiratory particulates. They do not apply to powered air-purifying respirators (PAPRs). The particulate respirator will have an N, R, or P designation along with an efficiency rating such as 95, 99, or 100. Some examples include N95 and N100 disposable facepiece respirators and a P100 cartridge.  Please make note of these designations as you make your selection for the respirator suitable for your job task.

N, R, P Designations

| Use | When |
| --- | --- |
| N | No oil is present in the air. |
| R | Oil is present, but only for a single shift or 8 hours of continuous or intermittent use. Note: Re-use beyond a single shift or 8 hours is not recommended. |
| P | Oil is present, but follow the manufacturer’s time use limitations if you want to re-use these. |

100, 99, and 95 Efficiency Ratings*

| If the efficiency level is: | This means |
| --- | --- |
| 100 | The filter is expected to trap 99.97 particles out of every 100. It is as efficient as a High Efficiency Particulate Air (HEPA) filter. |
| 99 | The filter is expected to trap 99 particles out of every 100. |
| 95 | The filter will trap 95 particles out of every 100. |

*The table shows how efficient the respirator’s filter capacity is expected to be against particles that are at least 0.3 micrometers.  The higher the number, the higher the efficiency expected.